## Slide 1: SCH Practical & Precision Assessments
An impact assessment approach for schistosomiasis programmes
Urine Sample Collection, Processing and Diagnostics

## Slide 2: Training Goals
In this module you will learn the following steps in the laboratory methods
Macroscopic observation
Hemastix reagent strip
Urine filtration (UF)

## Slide 3: Safety Precautions
The urine should be considered potentially infectious; wear gloves and lab coats
Benches, instruments and equipment should be routinely decontaminated with disinfectants after use
Materials contaminated with infectious waste should be disinfected before disposal
Drinking or eating during laboratory procedures is prohibited
Appropriate disinfectant(s) should be used for disposal of contaminated materials, wooden spatulas and specimen containers and for cleaning of workbenches
Used specimen containers must be disinfected before washing

## Slide 4: Equipment required
Protective clothing:
Gloves
Laboratory Coat
Closed toe shoes
Blood in urine:
Urine pots (20ml)
Hemastix reagent strip
Hemastix pot with scale
Urine Filtration:
Filter Holder
Tweezers/Forceps
Syringe, plastic, 10ml
Microscope glass slides
Lugol’s Iodine (5% solution)
Nuclepore Membrane Filter, 13mm diameter / pore size 12µm
Microscopic examination:
Microscope
Hand tally counter
Disinfectants and waste disposal:
Bucket (to discard urine)
1% hypochlorite solution (domestic bleach)
Methylated Spirit
Medicated soap
Rubber washing gloves
Disinfectant wipes
Waste container (containing disinfectant)
Sample labelling and data entry:
Barcodes
Phone with pre-installed results form/ case record form

## Slide 5: Macroscopic observation
Purpose: the observation is to identify visible blood in urine (macrohaematuria)
You need to record if you can see blood in the specimen
Macroscopic haematuria
YES, visible blood in urine
Dark urine
NO, visible blood in urine

## Slide 6: Hemastix reagent strip
Purpose: the hemastix reagent strip (or dipstick) tests for non-visible blood in urine (microhaematuria)
Ensure this is done within 2 hours of collection
(3)
(4)
Ensure you are wearing gloves
Remove one strip from the bottle and stick the ‘dipstick barcode’ on the urine specimen container
Completely immerse reagent areas of strip into urine specimen for a few seconds
When removing the strip, run its edge against the rim of the container to remove any excess urine

## Slide 7: Hemastix reagent strip
Put the strip horizontally on the table, or on top of the urine container, so that the chemicals do not mix together
Read the strip between 1-2 mins after it has been dipped in the urine. Any colour changes that appear after 2 minutes are of no diagnostic value and should be ignored
(5)

## Slide 8: Hemastix reagent strip
Match the colour of the strip with the colour chart on the bottle label
DO NOT LAY THE STRIP ON THE COLOUR CHART AS THIS WILL SOIL THE CHART
The order of readings on the colour chart will match the order of results to enter on phone i.e
0 = None (negative)
1 = Trace/moderate non-haemolysed
2 = Trace haemolysed
3 = +
4 = ++
5 = +++
(7)

## Slide 9: Urine filtration
Equipment
General equipment – gloves, microscopes etc
Urine container (250ml) = REUSABLE
Swinnex filter holder = REUSABLE
Tweezers/forceps = REUSABLE
Syringe, plastic, 10ml = REUSABLE
Nuclepore membrane filter, 13mm diameter and pore size 12µm - 25µm
Microscope glass slides = REUSABLE
Lugol’s iodine (5% solution)
Potentially: cellophane strips (hydrophilic, 30 - 50µm thick), soaked in glycerol

## Slide 10
Preparation, evening before the survey:
Ensure the filter holders and syringes are well cleaned and dry
Unscrew the filter holder and insert a Nuclepore filter between the two parts of the filter holder
Make sure it is correctly held in place before screwing the unit together again
Purpose: the urine filtration identifies presence and number of eggs for Schistosoma haematobium (prevalence and intensity of infection)
(2)
(3)
Urine filtration

## Slide 11
Carrying out the procedure
Shake and mix urine, then draw 10mls urine into the syringe (or if less than 10mls use draw up all of it)
Attach filter holder (with filter inside)
Keeping syringe vertical, press plunger down to push all urine into a bucket.
Detach filter unit, draw air into the syringe, reattach unit and expel air again
Unscrew filter holder and use pair of tweezers to remove filter and place on microscope glass (top side of filter always facing upwards)
(1)
(2)
(4)
(5)
Urine filtration

## Slide 12
Add one drop of Lugol’s iodine and wait 15 seconds before reading under the microscope
Perform microscopy: see slide 13
If the slides are kept for quality control (recommended), cover the stained filter with a glycerol soaked cellophane strip. Potentially add 4% formalin or SAF-solution for longer storage.
If slides are stored, keep them in the fridge to avoid hatching of eggs.
(6)
(7)
(8)
Urine filtration

## Slide 13: Urine Filtration Microscopy
Use x10 objective for scanning the slide, potentially use higher magnification for checking individual eggs (e.g. 40x)
Starting in one corner of the sample, systematically scan the WHOLE sample in a ‘zig zag’ scheme
When moving to a new row, keep a small microscopic field overlap: an object in the corner of the field is chosen and is brought towards the opposite side of the field. Then the second field is examined.
Count ALL eggs present using hand tally counters. Make sure not to confuse counters for different species.
(2)
(3)

## Slide 14: Quality control: urine filtration
10% of all slides are randomly selected and re-examined by a more experienced technician
Results are considered discrepant if the egg count differences are:
    For counts below 50 eggs: more than ±5 eggs
    For counts >50 eggs: more than ±10%
    Differing between egg-positive and egg-negative
Discrepant slides are re-read again by a third technician and final decision on results are made based on all three readings
If more than 50% of QC slides are discrepant on several days, the lead technician should conduct re-training and discuss with the survey team lead about suitable consequences.

## Slide 15: Field readiness
Before the start of the survey, perform a half-day practice session as diagnostics refresher (or a full day if it is the team’s first time) AND 1 full day of practice as pilot in a nearby school
Half-Day Refresher:
Establish who are the senior and most experienced lab technicians. Assess performance additionally to years of experience.
Check material, discuss SOPs and lab flow
Perform initial round of diagnosis with all steps as the whole team together

## Slide 16
Practice day (Pilot):
Assign reading technicians and QC readers
Prepare adequate number of samples, so that every reader has at least 4 slides
After initial read, immediately give the slides to the next technician. Make sure there is no copying of results.
Compare results according to QC criteria.
All slides on which QC criteria are not met should be re-read by the QC reader and results should be discussed with the original readers. Once consensus is reached, discuss results with the whole team present.
After initiation of field activities, check QC each day to look out for systematically underperforming team members. Repeat training steps if possible. If lack of adequate performance persists after 1-2 weeks, discuss possible replacement of staff with managers.
Field readiness

## Slide 17: Questions?