## Slide 1: SCH Practical & Precision Assessments
An impact assessment approach for schistosomiasis programmes
Stool Processing and Diagnostics

## Slide 2: Training Goals
In this module you will learn the following steps in the laboratory methods
Kato-Katz thick smear

## Slide 3: Safety Precautions
Stool should be considered potentially infectious
Wear gloves and lab coats whenever handling stool samples
Benches, instruments and equipment should be routinely decontaminated with disinfectants after use
Materials contaminated with infectious waste should be disinfected before disposal
Drinking or eating during laboratory procedures is prohibited
Appropriate disinfectant(s) should be used for disposal of contaminated materials, wooden spatulas and specimen containers and for cleaning of workbenches
Used specimen containers must be disinfected before washing

## Slide 4: Equipment required
Protective clothing:
Gloves
Laboratory Coat
Closed toe shoes
Kato-Katz:
Stool sample in container
Cellophane sheets (hydrophilic, 30 - 50µm thick)
Malachite green (or methylene blue)
Metal sieve (Endecott sieve) with 200 - 250µm mesh size OR nylon mesh with up to 300µm mesh size
Microscopic glass slides
Glycerol
Slide boxes
Newspapers
Wooden or plastic spatulas/ applicators
Forceps
Kato-Katz plastic template (6mm hole on a 1.5mm thick template, delivering 41.7mg of faeces)
Microscopic examination:
Microscope
Hand tally counter
Disinfectants and waste disposal:
Bucket (to discard stool into and then into latrine)
1% hypochlorite solution (domestic bleach)
Methylated Spirit
Medicated soap
Rubber washing gloves
Disinfectant wipes
Waste container (containing disinfectant)
Sample labelling and data entry:
Barcodes (if being used)
Phone with pre-installed results form/ case record form

## Slide 5: Kato-Katz thick smear preparation: pre-survey
Preparation prior to the survey:
Creating the reagent
  Dilute 100ml of distilled water in 3g of malachite green/methylene blue (“stock solution”)
  Dilute 60ml of glycerine in 40ml of distilled water, creating 60% glycerol solution
  Take 1 ml of “stock solution” and add to 60% glycerol, creating “working solution”
Cut cellophane into 25mm x 30mm pieces
Soak pieces in “working solution” for at least 24 hours

## Slide 6: Kato-Katz thick smear - processing
Place two glass slides next to each other and label them with the sample number, then place a plastic template on each one.
Place a small amount of faeces and press through the metal sieve
Scrape the faecal sample from the under side of the metal sieve
With the template on top of the glass slide, fill in the hole and level the faeces off
2
4
3
Notes: If testing for STH, please add:
If hookworm is present in the area, the slide should be read within 60 minutes of processing

## Slide 7: Kato-Katz thick smear - processing
Place cellophane piece soaked in glycerol solution on top of faecal sample. Flip the slide upside down and press it against a firm surface to evenly spread the faeces in a circle. Slide sideways carefully when lifting to avoid separation of the cellophane
Let the slide clear (e.g. dry) with the cellophane upwards for 30 minutes (less if exposed to sunlight). If hookworm is present, the slide should be read within 60 minutes of processing
For one stool sample (slide A and B), each slide should be examined by different technicians, if possible.
5
Notes: If testing for STH, please add:
If hookworm is present in the area, the slide should be read within 60 minutes of processing

## Slide 8: Microscopy: Kato-Katz
Use x10 objective for scanning the slide, potentially use higher magnification for checking individual eggs (e.g. 40x)
Starting in one corner of the sample, systematically scan the WHOLE sample in a ‘zig zag’ scheme
When moving to a new row, keep a small microscopic field overlap: an object in the corner of the field is chosen and is brought towards the opposite side of the field. Then the second field is examined.
Count ALL eggs present using hand tally counters. Make sure not to confuse counters for different species.
2
3

## Slide 9: Quality control: Kato-Katz
10% of all slides (counting both slides A and B) are randomly selected and re-examined by a more experienced technician
Results are considered discrepant if the egg count differences are:
For counts below 100 eggs: more than ±10 eggs
For counts >100 eggs: more than ±20%
Differing between egg-positive and egg-negative
Discrepant slides are re-read again by a third technician and final decision on results are made based on all three readings
If more than 50% of QC slides are discrepant on several days, the lead technician should conduct re-training and discuss with the survey team lead about suitable consequences.
NOTE: Hookworm eggs will not be considered, as they are known to become transparent over time

## Slide 10: Field readiness
Before the start of the survey, perform a half-day practice session as a diagnostics refresher (or a full day if it is the team’s first time) AND 1 full day of practice as pilot in a nearby school
Refresher (half-day)
Establish who are the senior and most experienced lab technicians. Assess performance additionally to years of experience.
Check material, discuss SOPs and lab flow
Perform initial round of diagnosis with all steps as the whole team together

## Slide 11
Practice day (Pilot):
Assign reading technicians and QC readers
Prepare adequate number of samples, so that every reader has at least 4 slides
After initial read, immediately give the slides to the next technician. Make sure there is no copying of results.
Compare results according to QC criteria (slide 18).
All slides on which QC criteria are not met should be re-read by the QC reader/s and results should be discussed with the original readers. Once consensus is reached, discuss results with the whole team present.
After initiation of field activities, check QC each day to look out for systematically underperforming team members. Repeat training steps if possible. If lack of adequate performance persists after 1-2 weeks, discuss possible replacement of staff with managers.
Field readiness

## Slide 12: Questions?